## Slide 1: Project 05: Hydrogen Sloshing on Ansys FLUENT
Team Members
Dated: 16th February 2026
Narmeen Asif
Daniel Pineda Estrada
Taha Javed
Decency Chukwuemeka Ukonu
Muhammad Ehab Bin Nauman
Aly Morsy
Pegah Aghasikhani

## Slide 2: Executive Summary – Multiphase Sloshing Simulation
🔷 Objective: Transient CFD analysis of liquid–gas sloshing in a partially filled storage tank under harmonic excitation, focusing on interface dynamics, pressure loads and thermal effects.
🔷 Modeling Approach: • 2D tank (~75% water) • Harmonic motion (f = 0.89 Hz) • Transient pressure-based solver (ANSYS Fluent) • VOF + k–ω SST + Energy equation
🔷 Numerical Verification: • 4 structured meshes (1k–24k cells) • Monitored: average upper wall pressure • 1.8% error (Medium vs Fine) • Medium mesh selected for post-processing
🔷 Key Results • Stable sloshing for more than one cycle (2 s) • Pressure amplification near walls • Similar wave behaviour for both gases • Suitable for structural safety assessment

## Slide 3: Motivation for the Study
Sloshing - Motion of a Liquid’s Free Surface, due to tank movement
Fundamental fluid phenomenon in many real-world systems
Talking about Hydrogen…
Applications:
Transport Vehicles
Aerospace Rockets
Cryogenic Storage Tanks

## Slide 4: What are the problems in such applications?
Liquid impacts wall → sudden deceleration
Momentum change → impact force
Local pressure rise (possible temperature increase)
Structural stress on tank
Gas compression → enhanced boil-off
Rocket/Vehicle functions failure risk
​

## Slide 5: Case Description (Hydrogen Sloshing in a Tank)
Transient CFD Simulation to study Fluid Interface, Liquid-Gas Regions, Heat transfer from Tank to Atmosphere, Wave Behavior, Fluid-Wall Interactions
0.35 m
0.75 m
Approx ~75 % H20
Harmonic Motion
For simplicity, hydrogen is not used in the study; instead, water and two surrogate gases are considered, one denser than the other

## Slide 6: Work Distribution
Pre-Processing & Numerical Solution
Post-Processing
Daniel Pineda Estrada
Numerical Grid Independence Study
Muhammad Ehab Nauman
Ali Morsy
Pegah Aghasikhani
Narmeen Asif
Decency Chukwuemeka UKONU
Taha Javed

## Slide 7: Timeline of the Project
Week 01 (12/01 – 16/01)
Project onboarding & planning: Understanding project description, defining tasks, assigning roles
Week 02 (19/01 – 23/01)
Geometry Cleanup and Meshing: Edge and face sizing, quality checks defining fluid/solid zones, motion setup
Week 03 (26/01 – 30/01)
Week 04 (02/02 – 06/02)
Week 05 (09/02 – 13/02)
Mesh Independence Study, Presentation preparation, cross-checking results, team integration
Post-Processing: Extracting contours, vectors, pressure plots, heat flux, interface evolution
Solver Setup: Physics models, boundary conditions, time‑step selection

## Slide 8: Geometry and Meshing
Simple 2D Geometry Featuring Specific Edges, Meshed Using Hexahedral Elements
Edge Sizing
Horizontal walls – 50 Divisions
Vertical walls – 10 Divisions
Face Sizing with element size = 0.005m
Skewness ~ 0.5, Orthogonality ~ 0.95

## Slide 9: Edge Sizing
Refined mesh on specific edges using edge sizing
10 divisions used
If we merge the edges in geometry setup, it could lead to some non-structured meshes in center

## Slide 10: Solver Setting
Solver Configuration & Global Settings (General)
Solver type: Pressure-based
suitable for incompressible, appropriate for water–gas sloshing simulations
Why transient simulation?
To capture:
time-dependent sloshing motion
interface deformation under dynamic excitation
Equations solved for: • Flow • Volume Fraction • Turbulence • Energy
Notes: The simulation was performed using the pressure-based solver with absolute velocity formulation. A transient 2D planar configuration was selected to capture the sloshing dynamics. Gravity was enabled in the negative y-direction to represent realistic liquid–gas stratification.
The horizontal acceleration was introduced using a time-dependent expression to model the tank excitation.

## Slide 11: Solver Setting
Tthermophysical properties (Materials)
 | Gas 1 | Gas 2
Density | 3.99 kg/m3 | 6 kg/m3
Cp | 710 J/(kg.K) | 670 J/(kg.K)
Thermal Conductivity | 0.015 W/(m.K) | 0.013 W/(m.K)
Dynamic Viscosity | 1.55e-5 (Pa.s) | 1.5e-5 (Pa.s)
Water was also selected from FLUENT database
Notes: Next step we defined the thermophysical properties of the materials. Water was selected directly from the Fluent database. Two surrogate gases were implemented to study the effect of gas density on sloshing behaviour. Gas 2 has a higher density than Gas 1, allowing comparison of interface response under different gas environments.

## Slide 12: Solver Setting
Physics Models: Turbulence & Multiphase Model
K-omega SST Model is used for Turbulent Regime
Notes: For the physics models, we used the Volume of Fluid model to capture the liquid–gas interface. Two Eulerian phases were defined: water as the 2ndary phase and the surrogate gas as the primary phase.
For turbulence modelling, the SST k–omega model was selected to accurately resolve near-wall effects and transient flow behaviour during sloshing.
The implicit scheme is more stable for larger time steps, but the explicit formulation offers better interface resolution when the time step is sufficiently small, which was the case in our simulation. The explicit scheme improves numerical stability for interface capturing and allows better control of the Courant number, which is important in transient multiphase simulations.

## Slide 13: Solver Setting
Boundary Conditions
For all the tank walls, convection boundary condition was applied to model external heat exchange with the environment.
Notes: For the tank walls, a convection boundary condition was applied to model heat exchange with the surrounding environment. A heat transfer coefficient of 5 W per square meter Kelvin and an ambient temperature of 293 Kelvin were specified. Convection better represents realistic heat exchange with the external environment compared to a fixed temperature or heat flux condition.

## Slide 14: Solver Setting
Solution Methods
Numerical Strategy
PISO for transient pressure-velocity coupling
PRESTO for gravity-driven pressure field
Second-order schemes for improved accuracy
Geo-Reconstruct for sharp interface tracking
Under-Relaxation Factors
Pressure = 0.3
Momentum = 0.7
k, ω = 0.8
Energy = 1
Notes: For the solution methods, the PISO scheme was selected for pressure–velocity coupling, as it improves accuracy in transient simulations with rapidly changing flow fields.
For spatial discretization, PRESTO was used for pressure to better handle gravity effects. Momentum, turbulence, and energy equations were discretized using second-order upwind schemes to increase spatial accuracy.
The Geo-Reconstruct scheme was applied for volume fraction to ensure sharp interface capturing in the VOF model.
PISO performs multiple correction steps per time step, which improves transient solution stability and accuracy.
PRESTO improves pressure interpolation in flows influenced by gravity and free-surface motion.
Second-order schemes reduce numerical diffusion and improve solution accuracy compared to first-order schemes.
Conservative relaxation was used to ensure stable convergence under transient multiphase conditions. Because our simulation is transient, under-relaxation factors are less dominant than in steady simulations. In transient simulations:
Stability is mainly controlled by time step size
Under-relaxation still helps numerical stability, but is secondary

## Slide 15
a(𝑡) = 𝐴𝜔2sin(𝜔𝑡)
A is the amplitude of displacement (meters),
𝜔 the angular frequency (rad/s)
Frequency f of 0.89 Hz.
We found angular velocity through 𝑓 = 𝜔/2π
Also, T is time for one oscillation,
No reference frame or mesh motion was activated
Solver Setting
Harmonic Motion (Sinusoidal Acceleration)

## Slide 16
For Number of Time Steps
N = ​​​ , Tsim is required simulation time = 1.16s to at least have one oscillation cycle.
x(t) = 𝐴sin(𝜔𝑡), where x is displacement, using this.
We got:
Velocity is the first derivative of displacement:
Differentiate:
Timestep was calculated using:
Co =
Co was set as 0.25
Element Size (m) | Timestep Size | Number of Timesteps | Number of Iterations
0.005 m | 0.005 | ~230 | ~400
Solver Setting
Timesteps calculation to get desired simulation time

## Slide 17
Solver Setting
Initialization and Patching
Standard initialization - Water patched to 70% fill level - Sharp initial interface defined

## Slide 18: Post Processing

## Slide 19: Numerical Convergence Analysis A
Residuals of Surrogate Gas 1
Tight Iterations
20 step workout
Solver refines the math before moving on.
Sawtooth Drop
Residual Nose-Dive
Error levels drop up to 3+ orders of magnitude every 0.005s.
Energy < 10-6
Deep convergence in the Energy equation. Heat transfer results aren't just guesses. They’re reliable.
Thermal Confidence

## Slide 20: Numerical Convergence Analysis B
Tighter Iterations
20 step workout
Higher gas density. Solver refines the math before moving on.
Sawtooth Drop
Residual Nose-Dive
Error levels drop up to 3+ orders of magnitude every 0.005s.
Energy < 10-6
Deep convergence in the Energy equation. Heat transfer results aren't just guesses. They’re reliable.
Thermal Confidence
Residuals of Surrogate Gas 2

## Slide 21: Temporal Stability & CFL Analysis
Stability Threshold
The 2s Milestone
Margin of Safety
At the 2s cycle mark, AVE_CFL is only 0.6. Comfortable buffer against numerical instability.
Temporal Precision
0.005s Step Size
Resolving high-velocity sloshing without excessive cost.
CFL < 1.0 Limit
This acts as a speed limit to prevent the liquid interface from diverging.

## Slide 22: Quantitative Time Evolution Analysis (Surface Tracking)
Line1 at
0.25x
Line1 at
0.5x
Line1 at
0.75x
Iso-surface for vol_fraction = 0.5 (to track interface)

## Slide 23: Quantitative Time Evolution Analysis (Surface Tracking)
In one cycle (1.16s), the two surrogate gases 1 and 2 showed almost similar wave behavior in sloshing, the free surface at the three locations is almost identical over simulation time

## Slide 24: Quantitative Time Evolution Analysis (Pressure)
Average pressure on the upper wall showed almost identical behaviour for the two gases
The high spike is due to impact of the liquid on the upper wall in late simulation time

## Slide 25: Quantitative Time Evolution Analysis (Force)

## Slide 26: Quantitative Time Evolution Analysis (Heat Flux)
Heat flux through all tank walls (with natural convection BC's and thin wall model for 2D tank)

## Slide 27: Volume Fraction Contours Show Wave Formation
Notes: Initial idea was to do the simulation for 1.16 seconds but an extension to 2 seconds permits to see the breakage of the wave by the impact on the walls
What we want to see:
Free surface deformation, liquid impact on walls and ceiling. (helps calculate maximum wave height, sloshing severity or on more complicated cases the risk of hitting structural components.
Also help us evaluate compressibility effects (gas compressibility dampens sloshing)
Interface movement affects pressure oscillations
Do we have jet formation? Wave overturning? Assymetric filling patterns?
PLAY

## Slide 28: With little to no change in the qualitative behavior w.r.t surrogate gas 2
Notes: Surrogate gas 2 doubles surrogate gas 1 in density, but have the same viscosity and comparable CP and thermal conductivity

## Slide 29: What can we tell from the dynamic behavior?
Velocity vectors show a transient increase in magnitude upon contact with the wall.
Heavier and thicker phases resist more to changing velocities than lighter ones.
Notes: What we want to see
1. Circulation patterns inside the liquid
2. Wave propagation and direction
3. Vortices and recirculation zones
Do we have gentle slosh?, wave amplification?
PLAY
We can see strong momentum transfer (high velocities near walls), and high shear stress zones
Time of study doesn’t allow to see damping or energy dissipation due to viscosity or turbulence (important for cryogenic storage)

## Slide 30
Notes: Surrogate gas 1 movess lightly faster upon oscillation

## Slide 31: Pressure Amplifies Near Tank Walls
Useful to assess structural stresses, resonance behavior, and damping effect of the gas phase!
Notes: Static pressure represents the exact thermodynamic pressure on the substance.
Pressure within the system can be less than the atmospheric one leading to negative static pressure values
Goals:
Identify pressure peaks (local stress hotspots) -> structural safety and fatigue
Understand liquid-gas interaction (Dynamic variations due to motion) -> how hydrogen cushion influences pressure oscillations
Reveal wave motion!
For the future: Evaliate structural and design implications
PLAY
The contours reveal pressure amplification near the tank walls during oscillatory motion, reflecting the interaction between the liquid phase inertia and the compressible gas cushion. Essential for evaluating structural stresses, identifying resonance behavior, and understanding the damping effect of the gas phase

## Slide 32
Temperature contours shows achievement of thermodynamic equilibrium inside the tank in the very first moments of total runtime
Notes: Usually temperature could help us capture:
Thermal stratification(if any)
Heat transfer between phases.

## Slide 33: Principal remarks
Velocity describes fluid motion and momentum transfer
Volume fraction describes interface dynamics and sloshing severity
Temperature gives insight into thermal mixing and outside heat transfer
Pressure shows the fluid load distribution and transmission
Applications of the study and possible complementary studies:
Structural safety: Velocity and volume fraction could predict impact intensity on walls; pressure correlation: fatigue of the tank
Sloshing stability and wave resonance
Thermal mixing and stratification
Together, post-processing analysis provides the multiphase thermo-fluid physics

## Slide 34: Mesh Independence Study

## Slide 35: What is Mesh Independence?
CFD solutions depend on mesh resolution
Coarse mesh : faster but less accurate
Fine mesh : more accurate but expensive
Need to find a compromise
Mesh independence ensures accuracy, numerical stability, and reliable results

## Slide 36
Why Mesh Independence Study?
⚙️
Grid Resolution Impact
CFD solutions depend on mesh fineness
📊
Discretization Error
Spatial discretization introduces numerical errors
✓
Solution Verification
Ensures results are mesh-independent
🎯
Optimal Balance
Find accuracy vs. computational cost trade-off
Objective:
Verify grid-converged solution
Convergence achieved when:
• Error < 2% between meshes
• Results stable with refinement
• Quality metrics satisfied

## Slide 37
Methodology
Convergence Parameter
Monitored Variable:
Average Upper Wall Pressure
Reason for Selection:
• Direct indicator of sloshing impact
• Critical for structural analysis
• Sensitive to mesh resolution
Convergence Criterion
Error < 2%
Relative error between consecutive
mesh refinements
Analysis Process
1. Create Meshes
→
2. Run Simulations
→
3. Extract Pressure
→
4. Calculate Error

## Slide 38: Highly Coarse Mesh

## Slide 39: Coarse Mesh

## Slide 40: Medium Mesh

## Slide 41: Fine Mesh

## Slide 42: Grid Convergence
Timestep | Element size | No. of cells | Pressure (Pa) | Error | 
0.05 | 0.05 | 1000 | -520 | % | 
0.007 | 0.007 | 6000 | -566 | 0.088462 | 8.846154
0.005 | 0.005 | 11000 | -595 | 0.051237 | 5.123675
0.0035 | 0.0035 | 24000 | -606 | 0.018487 | 1.848739

## Slide 43: Pressure Plots
Medium
Fine
Coarse
Highly Coarse

## Slide 44
Mesh Quality
Mesh Type
Number of Cells
Element Size (m)
Min Orthogonality
Max Skewness
Highly Coarse
1,024
0.0098
0.66976
0.57131
Coarse
6,140
0.0070
0.78894
0.54604
Medium
11,649
0.0050
0.64564
0.55564
Fine
24,042
0.0035
0.70911
0.55251
✓ Quality Criteria Met: Orthogonality > 0.15, Skewness < 0.95.

## Slide 45
Grid Convergence
Average Upper Wall Pressure vs. Mesh Density
1024
-520 Pa
6140
-566 Pa
11649
-595 Pa
24042
-606 Pa
Number of Cells
Pressure (Pa)
Convergence
Zone

## Slide 46
Mesh Quality Comparison
All meshes meet quality criteria for accurate CFD analysis. Quality improves with refinement, ensuring reliable results.
Metric
Target
Coarse
Medium
Fine
Orthogonal Quality
> 0.15
0.970
0.997
0.998
Skewness
< 0.95
0.153
0.028
0.021
Aspect Ratio
< 100
< 25
< 20
< 18
Mesh Representations
Coarse
6,140 cells
Medium
11,649 cells
Fine
24,042 cells

## Slide 47
Mesh Independence Summary
Relative error of 1.8% between Medium and Fine meshes (< 2% criterion)
All quality metrics satisfied: Orthogonality > 0.15, Skewness < 0.95
Medium mesh provides accuracy with reasonable computational cost
Medium mesh (11,649 cells) selected as optimal configuration
Further refinement showed < 2% change, confirming mesh independence
Thank you for your attention!